## Slide 1: Sector Coupling of a Local Energy System Influence of Location Dependent Parameters
Frida Revheim, Daniel Schwabeneder, Georg Lettner
TU Wien ESEA
revheim@eeg.tuwien.ac.at
1st IAEE Online Conference
08.06.21

## Slide 2
Introduction and motivation
Methodology
  Model development
  Use cases
Preliminary results
Further work
Introduction

## Slide 3: Idea and motivation
  Sector coupling could be part of a solution to reach GHG emission targets
    Green hydrogen and green heat
    Curtailment reduction
  Potential benefits of sector coupling will depend on system location and location-specific variables
    Electricity generation
    Energy demands
    Available fuel options
  Comparative analysis is performed to evaluate the influence of location-dependent parameters on system operation and profitability
  Two key motivational factors:
    Ensure continued implementation and operation of RES
    Reduce GHG emissions

## Slide 4: Investigated KPIs
  Investigated KPIs:
    Profitability
    Degree of utilization of implemented technologies
    GHG emission reduction potential
    Renewable energy self-reliance
    External energy purchase
    Curtailment reduction

## Slide 5: Methodology – model development
  Optimization model of sector coupled system developed in Julia
  Operational model, not considering investment costs
  Objective: optimize system operation to maximize profit, while meeting energy demands and following constraints at all times
  Revenues:
    Selling electricity to the electricity market
    Selling hydrogen to the gas market
    Selling hydrogen to industry/mobility
  Costs:
    Buying electricity to cover electricity demand
    Buying electricity to feed into heat pump
    Buying heat produced by alternative heat source to cover heat demand
    Buying natural gas to cover gas demand

## Slide 6: Methodology – model development
  Investigated system includes both P2H and P2G technology
  Three different use cases
    Austria, Norway, Spain
  Location-dependent parameters as input for model
      Electricity generation from wind farm
      Local electricity, heat and gas demand
      Electricity prices, gas prices, price for alternatively produced heat
      Alternatives to green heat and the corresponding emissions
      Electricity mix

## Slide 7: Methodology – use cases
Austrian use case[1]:
Neusiedl am See region
4290 households
Wind farm with 32 MW installed capacity
Majority of heat demand covered by gas
Norwegian use case[1]:
Åfjord municipality
1961 households
Wind farm with 57.5 MW installed capacity
Majority of heat demand covered by electricity
No gas demand considered
Spanish use case[1]:
Municipalities of Isar,Las Quintanillas,Rabé de las Calzadasandand Estepar
1000 households
Wind farm with 31.5 MW installed capacity
Majority of heat demand covered by gas
No district heating demand considered

## Slide 8: Methodology – scenarios
  Three scenarios investigated for each use case
    Scenario 1
      Electricity demand  electricity generated by wind farm and electricity bought from electricity market
      Heat demand  heat bought from an alternative heat source
      Gas demand  natural gas bought from the gas grid
    Scenario 2
      Electricity demand  electricity generated by wind farm and electricity bought from electricity market
      Gas-using customers assumed connected to district heating grid
      Heat pump scaled according to district heating demand
    Scenario 3
      Electricity demand  electricity generated by wind farm and electricity bought from electricity market
      Gas-using customers assumed switching to green hydrogen
      Heat pump scaled according to district heating demand
      Electrolyzer scaled according to gas demand
Scenario 1
Wind farm
Scenario 3
Wind farm
Heat pump
Electrolyzer
Scenario 2
Wind farm
Heat pump

## Slide 9: Results – economic, AT use case
Chart: Economic results - Austrian use case
| Total profit | Revenue windmill | Revenue electrolyser | Total revenue | Cost heat pump | Cost electricity demand | Cost heat demand | Cost gas demand | Total cost
Austria Scenario 1 | 1242.3672 | 2196.2353 | 0 | 2196.2353 | 0 | -206.4157 | -256.0223 | -382.2186 | -844.6565
Austria Scenario 2 | 1282.4573 | 2064.9772 | 0 | 2064.9772 | 0 | -236.0884 | -437.2199 | 0 | -673.3083
Austria Scenario 3 | 3452.5414 | 1276.4731 | 3367.8302 | 4644.3033 | -9.8188 | -602.6404 | -84.4851 | -382.2186 | -1079.1628
System is profitable in all investigated scenarios
Introduction of electrolyzer significantly influences profit
Introduction of heat pump reduces costs related to covering the heat demand

## Slide 10: Results – economic, NO use case
System is profitable in all investigated scenarios
Slight increase in profitability due to heat pump implementation
No electrolyzer implemented (no gas demand)
Chart: Economic results - Norwegian use case
| Total profit | Revenue windmill | Revenue electrolyser | Total revenue | Cost heat pump | Cost electricity demand | Cost heat demand | Cost gas demand | Total cost
Norway Scenario 1 | 3257.6268 | 3517.0165 | 0 | 3517.0165 | 0 | -106.1311 | -43.6721 | 0 | -149.8033
Norway Scenario 2 | 3275.646 | 3498.2045 | 0 | 3498.2045 | -0.010033 | -107.5554 | -5.4067 | 0 | -112.9721
Norway Scenario 3 | 3275.646 | 3498.2045 | 0 | 3498.2045 | -0.010033 | -107.5554 | -5.4067 | 0 | -112.9721

## Slide 11: Results – economic, ES use case
System is profitable in all investigated scenarios
Slight increase in profitability due to heat pump implementation
No heat pump implemented in scenario 3 (no district heating demand)
Chart: Economic results - Spanish use case
| Total profit | Revenue windmill | Revenue electrolyser | Total revenue | Cost heat pump | Cost electricity demand | Cost heat demand | Cost gas demand | Total cost
Spain Scenario 1 | 3109.4078 | 3258.6879 | 0 | 3258.6879 | 0 | -0.32157 | 0 | -39.7469 | -40.0685
Spain Scenario 2 | 3109.0551 | 3243.9366 | 0 | 3243.9366 | 0 | -0.32157 | -25.3484 | 0 | -25.6699
Spain Scenario 3 | 3109.4078 | 3258.6879 | 0 | 3258.6879 | 0 | -0.32157 | 0 | -39.7469 | -40.0685

## Slide 12: Utilization of implemented technologies to cover demands – Austria scenario 3
Overview of technology utilization in Austrian use case – scenario 3
Generated electricity is either sold, used to cover demand or fed into electrolyzer
Gas demand fully met by bought natural gas

## Slide 13: Utilization of implemented technology to cover heat demand
Focusing on heat demand originally covered by district heating and gas
Heat demand coverage in scenario 3
  AT: Heat pump and electrolyzer
  NO: heat pump
  ES: electrolyzer
Excluding heat demand covered by electricity

## Slide 14: Results KPI – GHG emission reduction potential
Chart: Reduced GHG emissions [ton CO2]
| Scenario 1 | Scenario 2 | Scenario 3 | Scenario 1 | Scenario 2 | Scenario 3 | Scenario 1 | Scenario 2 | Scenario 3 | Austria | Norway | Spain
Electricity demand | 1710.7626 | 1650.4476 | 1070.0131 | 968.0312 | 967.5261 | 967.5261 | 420.5672 | 420.5672 | 420.5672
Heat demand | 0 | 4473.9232 | 2836.8824 | 0 | -0.0037327 | -0.0037327 | 0 | 307.1392 | 0
Gas demand | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Significant emission reduction potential
Reduction depending on:
  Size of technology
  Electricity mix
  Alternative fuel (natural gas, bio pellets)
All green hydrogen sold to market  no emission reduction achieved

## Slide 15: Results KPI – renewable energy self-reliance
Majority of electricity demand covered by electricity generated by wind farm
Implementation of electrolyzer reduces degree of electricity self-reliance
Introduction of heat pump can significantly affect degree of heat energy self-reliance
Chart: Electricity demand
| Scenario 1 | Scenario 2 | Scenario 3 | Scenario 1 | Scenario 2 | Scenario 3 | Scenario 1 | Scenario 2 | Scenario 3 | Austria | Norway | Spain
Electricity generated by wind farm | 0.83958 | 0.80998 | 0.52513 | 0.96409 | 0.96359 | 0.96359 | 0.99948 | 0.99948 | 0.99948
Chart: Heat demand
| Scenario 1 | Scenario 2 | Scenario 3 | Scenario 1 | Scenario 2 | Scenario 3 | Scenario 1 | Scenario 2 | Scenario 3 | Austria | Norway | Spain
Heat produced by heat pump | 0 | 0.38044 | 0.12518 | 0 | 0.87632 | 0.87632 | 0 | 0.45805 | 0
Waste heat from electrolysis | 0 | 0 | 0.54479 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 16: Results KPI – external energy purchase
Clear correlation with degree of energy self-reliance
Coverage of gas demand fully dependent on natural gas purchase
Amount of electricity bought from the grid depend on utilization and size of implemented technologies
Chart: Energy bought from external sources
| Scenario 1 | Scenario 2 | Scenario 3 | Scenario 1 | Scenario 2 | Scenario 3 | Scenario 1 | Scenario 2 | Scenario 3 | Austria | Norway | Spain
Electricity | 3113.1575 | 3687.5861 | 9422.1008 | 1163.4279 | 1179.8398 | 1179.8398 | 2.5294 | 2.5294 | 2.5294
Heat | 9696.518 | 16559.1463 | 3199.7637 | 1034.1493 | 128.0298 | 128.0298 | 0 | 826.3763 | 0
Natural gas | 17030.6355 | 0 | 17030.6355 | 0 | 0 | 0 | 1524.4484 | 0 | 1524.4484

## Slide 17: Results KPI – curtailment reduction
Curtailment due to negative electricity prices
  No curtailment in NO and ES
Curtailment reduced with heat pump and electrolyzer implemented
Chart: Reduction of curtailment in Austrian use case compared to Scenario 1
| Scenario 2 | Scenario 3
Reduction of curtailment in Austrian use case compared to Scenario 1 | 0.34114 | 0.46303

## Slide 18: Concluding remarks and further work
  Utilization of sector coupling concepts has the potential to reduce GHG emissions, increase degree of energy self-reliance and reduce curtailment
  Benefits of sector coupling depend on local conditions
  Further work could investigate
    Optimal system topology when considering investment costs
    Impact of local policy levers on influential parameters (e.g. electricity generation, energy demand, available fuel options)

## Slide 19: References and acknowledgements
This work is done in the “ThermaFLEX” project [2] and is supported with the funds from the Climate and Energy Fund and implemented in the framework of the RTI-initiative “Flagship region Energy” within Green Energy Lab.
  [1] Energy Data, EuroStat, https://ec.europa.eu/eurostat/web/energy/data
  [2] ThermaFLEX, Green Energy Lab, https://greenenergylab.at/en/projects/thermaflex/

## Slide 20
Frida Revheim
TU Wien
Energy Economic Group, EEG
Gußhausstraße 25-29 / E370-3
1040 Vienna, Austria
Email: revheim@eeg.tuwien.ac.at
Web: http://www.eeg.tuwien.ac.at
Thank you!