## Slide 1: POTENTIAL OF ELECTRIC VEHICLES TO OVERCOME TRANSMISSION LINE CONGESTIONS AND BALANCE REDISPATCH NEEDS
A CASE STUDY FOR THE AUSTRIAN CONTROL AREA
Christoph Loschan, Carlo Corinaldesi, Georg Lettner
(TU Wien – Energy Economics Group)
1st IAEE Online Conference
7.6.2021

## Slide 2: Overview
Motivation & Introduction
1
2
2.2
Aggregation
Dispatch
Redispatch
2.1
Model Formulation
Results
3
2.3

## Slide 3: Introduction & Motivation
Dispatch
Market-based (Merit Order)
Congestion
temporary overload
Redispatch
Power increase/decrease of power plants
> Volatile RESE generation
> geographical unequal distribution
> EV Demand:
simultaneity not correlated to generation
No allocation of transfer capacities within a bidding zone
Chart: Redispatch costs in Austria in M€
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
Österreich | 1.7 | 1.1 | 5.4 | 4.4 | 23.2 | 28.5 | 92.1 | 118.3 | 147.3 | 134 | 19.8

## Slide 4: Motivation & Research question
Research Question: Can we use a Demand-side-management of Electric vehicles charging processes to compensate redispatch needs?
Pairwise power increase/decrease
Th. power plants (50 MW+)

## Slide 5: Model Overview
Aggregation
of the model-input
Dispatch
Market-based
Disaggregation
of balancing groups
Charging profiles
Balancing groups (BGs)
Without transmission lines (except interconnector & FBMC)
Objective: OV cost minimisation
17 BGs in Austria
Redispatch
Within Austria
Objective: Redispatch costs minimisation
Balance redispatch needs, overcome congestions
all transmission lines (NTC & power flow)
PP usage, RESE curtailment, storage usage, unchanged from Dispatch
Th. PP regulation
Additional RESE curtailment
EV Demand-side-management
Charging processes -> charging types (per BG)
Austria 9 (from 17) BGs
Th. PP, RESE, storages

## Slide 6: Model Formulation
Aggregation
Statistical data
  one charge per week
  13 900 km/a
  16 kWh/100 km
Statistical values of charging behaviour [2]
Charging processes
  aggregate -> 6 different charging types

Plugged-in EVS
Chart: Hour of the day in h
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
user profile night 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2
user profile day 2 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
user profile night 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
user profile peak 1 | 2 | 2 | 2 | 2
user profile day 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
user profile peak 2 | 2 | 2 | 2 | 2
Chart: Hour of the day in h
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
user profile night 1 | 9.6521 | 9.6521 | 9.6521 | 9.6521 | 44 | 44 | 44 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
user profile day 2 | 0 | 0 | 0 | 0 | 0 | 122.5714 | 122.5714 | 122.5714 | 10.7551 | 10.7551 | 10.7551 | 10.7551 | 10.7551 | 10.7551 | 10.7551 | 10.7551 | 10.7551 | 10.7551 | 0 | 0 | 0 | 0 | 0 | 0
user profile night 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 56.5714 | 56.5714 | 56.5714 | 8.2732 | 8.2732 | 8.2732 | 8.2732 | 8.2732 | 8.2732
user profile peak 1 | 0 | 0 | 0 | 0 | 0 | 25.1429 | 25.1429 | 25.1429 | 22.0618 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
user profile day 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 40.8571 | 40.8571 | 40.8571 | 3.585 | 3.585 | 3.585 | 3.585 | 3.585 | 3.585 | 3.585 | 3.585 | 3.585 | 3.585 | 0 | 0
user profile peak 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 25.1429 | 25.1429 | 25.1429 | 22.0618 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Energy demand & DSM potential

## Slide 7: Model Formulation
Aggregation
}
pre optimisation calculation
Scenario depending: 0 or decision variable
DSM restrictions
Energy balance
Chart: Time of Day in h
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
user profile work 1 | 0 | 0 | 0 | 0 | 0 | 1225.7143 | 1225.7143 | 1225.7143 | 107.5515 | 107.5515 | 107.5515 | 107.5515 | 107.5515 | 107.5515 | 107.5515 | 107.5515 | 107.5515 | 107.5515 | 0 | 0 | 0 | 0 | 0 | 0
DSM potential | 0 | 0 | 0 | 0 | 0 | 1225.7143 | 1225.7143 | 1225.7143 | 2343.8771 | 2343.8771 | 2343.8771 | 2343.8771 | 2343.8771 | 2343.8771 | 2343.8771 | 2343.8771 | 2343.8771 | 2343.8771 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 8: Model overview – nodes & connections
Min. OV costs (Max. social welfare)
(th. PP, RESE, storages)
365 x 1 day optimisation
DC loadflow between spot markets
&
critical branches in Austria (FBMC)
[1]
Dispatch

## Slide 9: Model Formulation - Objective
365 x 1 Day-ahead optimisation
Dispatch
thermal generation
RESE
Storage usage
Not supplied energy

## Slide 10: Model Formulation - Constraints
for all RES types
Demand compensation
in every aggregated balancing group
thermal PP
Dispatch

## Slide 11: Model Formulation - Constraints
Technical &
Annual pattern storage constraints
Power flow between aggregated
balancing groups
NTC limit
Dispatch

## Slide 12: Model overview – nodes & connections
Min Redispatch costs in Austria
Detailed power plant allocation
EV DSM
Transmission grid & DC loadflow
[1]
Redispatch

## Slide 13: Model Formulation - Objective
Redispatch
Redispatch costs minimisation
in Austria
Redispatch costs for thermal PP
Redispatch costs for RESE

## Slide 14: Model Formulation - Constraints
Redispatch
Demand compensation
in every balancing group
In Austria
Dispatch = Constants
Redispatch = Decision variables

## Slide 15: Model Formulation - Constraints
Energy equilibrium
(power sum = const.)
Redispatch

## Slide 16: Results - Scenarios
ENTSO-E 2030 NT scenario
  Existing power plants and RES-E
  Electricity demand
3 Different scenarios
  200k EVs
  600k EVs
  2 Million EVs in Austria
3 Variants per scenario
  No DSM
  DSM usage in Redispatch
  DSM usage in Dispatch

## Slide 17: Results: 600k – Redispatch energy
Lower RESE curtailment
Less gas turbines

## Slide 18: Results – Costs - EV perspective
Energy is shifted to times with lower day-ahead prices
Without DSM:
Charging costs: 750 €
With DSM:
Charging costs: 709 €
-> 5,5 % cost reduction
24

## Slide 19: Results: 600k – Redispatch costs
6,6 % cost reduction

## Slide 20: Results: 600k – Redispatch CO2 emissions
20 % Redispatch caused CO2 emissions reduction

## Slide 21: Results: Summary & Conclusion
-2.5 % / -3 %
-20 % / +20 %
DSM during Redispatch
  Lowest RESE curtailment
  during Redispatch and Overall
  Lowest CO2 emissions
DSM during Dispatch ->
  Market based DSM
  Congestion more often
  Higher CO2 Emissions
Electric Vehicles
  High DSM potential (often available, whole year)
  Reduction of Redispatch costs
  Reduction of CO2 emissions
-7% / -2 %
-7% / +5%
-20 % / +13 %
-46% / +107 %

## Slide 22
Thank you!
This work is done in the ABS4TSO project [3], supported with the funds from the Austrian Research Promotion Agency (FFG).
Christoph Loschan, Carlo Corinaldesi, Georg Lettner
(TU Wien – Energy Economics Group)

## Slide 23: References
[1] Figure: L.Lang, The meaning of flow-based market coupling on redispatch measures in Austria, 2020, Energy Policy, Volume 136, https://doi.org/10.1016/j.enpol.2019.111061
[2] Statistic: C.Nelder, Electric Vehicles as Distributed Energy Resources, 2016, Project: EV-Grid Integration, https://www.researchgate.net/publication/324417842
[3] ABS4TSO project, https://projekte.ffg.at/projekt/2926652