## Slide 1
Impact assessment of willingness to pay on the installed and transmission capacities of renewable energy resources in Japan
Lu GAO, Yuki HIRUTA and Shuichi ASHINA
国立環境研究所
国立研究開発法人
NATIONAL INSTITUTE FOR ENVIRONMENTAL STUDIES
Center for Social and Environmental Systems Research,
National Institute for Environmental Studies (NIES)
The 1st IAEE Online Conference
JUNE 7th-9th, 2021
ACKNOWLEDGMENT: This research was supported by Environment Research and Technology Development Fund (2-1711) of Environmental Restoration and Conservation Agency and Ministry of the Environment Japan.

## Slide 2: Background
Renewable energy
Geographic Information
Wang (2014)
Weather Conditions
Shiraki (2014)
User Preference for RE
1
22% to 24%
(2030)
Energy Use Model
Fourth Strategic Energy Plan

## Slide 3: Background
Renewable energy
Fourth Strategic Energy Plan
Japan, 6.5 USD/month
China,2.7-3.3 USD/month
Willingness to pay
Korea,3.2 USD/month
2
22% to 24%
(2030)
Goto (2010)
Guo (2014)
Lee (2016)

## Slide 4: Background
Transmission capacities
Renewable energy potential
3
Wakiyama and Kuriyama (2018)

## Slide 5: Objective
How well WTP impact on generation and transmission of electricity from renewable energy resources ?
Incorporating WTP into a multi-regional optimal generation planning model
Japan
Up to 2050
10 Regions
4

## Slide 6: Framework
Build Acceptability Curve
WTP model
Forecast Median Willing to pay
Energy using model
Objective function: Min (Cost + Max (REcost))
Subject to :
Renewable energy potential
Natural condition
Economic condition

## Slide 7: Framework
Build Acceptability Curve
WTP model
Forecast Median Willing to pay
Energy using model
Objective function: Min (Cost + Max (REcost)
Subject to :
Renewable energy potential
Natural condition
Economic condition

## Slide 8: Methodology _ WTP function
WTPmed
Using meta-regression analysis to forecast the WTP
Gender:
Percentage of female share within total population (%)
Income:
Annual average household income (JPY)
(1)
5
Author | Survey Year | Survey Area | Median WTP JPY/(household·month) | Object analyzed
Nomura and Akai (2004) | 2000 | Japan | 1956 | WTP for promoting renewable
Baba and Tagashira (2002) | 2001 | Kagoshima | 239 | WTP for promoting green electricity
… | … | … | … | …
Data for Developed Statistic Models （17 observation）

## Slide 9: Methodology _ Acceptability curve
① Baseline (Weibull distribution)
Xt（WTP）
Y(%)
Y50%
Xbase
Xmed
(Xmed,Y50%)
(Xbase,Y50%)
Fbase(X)
F(X)
①
②
Where Fbase (X) is the base acceptability function, X is WTP in JPY/(household·month). a and b are assumed to 6.505 and 1.065 respectively.
② Shift in acceptability curve
Fig 1. Shift in acceptability curve
Where, F(X) is the acceptability function, Y50% is acceptability rates in 50%, X is WTP in JPY/(household·month), t is the year
(2)
(3)
6
Y: Acceptability

## Slide 10: Methodology _ Prediction of total WTP
7
WTP1
Y（WTP）
X (Acceptability, %)
Y（TWTP）
X (Acceptability, %)
X1
X2
X3
X1
X2
X3
WTP2
WTP3
TWTP1
TWTP2
TWTP3
Acceptability curve
Total WTP
TWTP1=WTP1×X1×N
N: The number of household
TWTP2=WTP2×X2×N
TWTP3=WTP3×X2×N
①
②
③
(2)
①
①
②
②
③
③

## Slide 11: Framework
Build Acceptability Curve
WTP model
Forecast Median Willing to pay
Energy using model
Objective function: Min (Cost + Max (REcost)
Subject to :
Renewable energy potential
Natural condition
Economic condition

## Slide 12: Methodology-Energy use (Model Structure)
6
ANRE: Agency for Natural Resources and Energy
Total cost Minimization
Supply O(t)
Capacity
DMND: Electricity demand
O: Electricity generation
STR: PH & SB FIX: Nuclear & hydro
TR: Energy transmission
Cc: capital cost, Co: O&M cost, Cf: fuel cost, Ct: transport cost, CCO2 : carbon cost, RE cost: cost for RE
Exogenous
Potential
Cost
TWTP: Total WTP; X:WTP
F(X):Acceptability function
HH: number of household
TL: transmission lines
Demand
(Ashina et al., 2007)
F(X): Acceptability function
: RE potential, estimated by Shiraki et al., 2011
Economic condition
Natural condition
Nuclear
Hydro
Gas
Oil
Coal
…
8

## Slide 13: Scenario Setting
Ref: Estimation the feasible energy mix without consideration the impact of WTP.
Scenario 1 : Estimation the feasible energy mix with consideration the impact of WTP. WTP is only used for increasing the capacity of renewable energy
Scenario 2 : Estimation the feasible energy mix with consideration the impact of WTP. WTP is only used for increasing the capacity of transmission line
9
Scenario 3 : Estimation the feasible energy mix with consideration the impact of WTP. WTP is used for increasing both capacity of renewable energy and transmission line (50% WTP for each item).

## Slide 14: Result _ Prediction of total WTP
For example, in Hokkaido, TWTP curve first increase and then decrease
The TWTP is increased from 491 to 1,388 billion JPY
9
TWTP in 2015
Acceptability rate (%)
TWTP [ Million JPY / year]
(b)
Ref (TWTP=0)
(c)
S1,S2, S3 (TWTP in 2050 )
(d)
(a)
Hokkaido _SSP1
Fig 4. Prediction of WTP from 2015-2050, (a) under SSP2 in Hokkaido by different acceptability rate, (b)-(d) the value of TWTP for different prefectures in the year 2015 and 2050.
Unit: Billion JPY/Year
250
60
40
20
10
5

## Slide 15: Result _ Influence of WTP on diffusion of RE in 2050
Fig 3. Electricity generation by renewable energy power plants under scenario Ref, 1, 2 and 3 in 2030
10
R3 is higher than other area, which is contributed by the higher income
In S1, the RE capacity is expected to be 15-fold than Ref
In S3, RE capacity is more than half of S1

## Slide 16: Result _ Power transmission capacity in 2050
Specific from Chugoku to Kansai, suggesting the great potential of increasing renewable transmission capacity in these lines
11
In S2 and S3, increase of RE transmission capacity, is expected to be 3-24-fold than Ref

## Slide 17: Result _ Carbon emission in 2050
Fig 5. Carbon emission under scenario 1 , 2 and 3 in 2050
12
By only RE and transmission, the carbon reduction target is still difficult to achieve in 2050.
Reduced carbon emission:
S3 ＞ S1 ＞S2

## Slide 18
Total WTP increase from 491 to 1388 billion JPY
Both consider the RE and transmission line can future increase the carbon emission reduction
The electricity generation from RE and transmission line with considering the WTP is expected to be 15-fold and 24-fold than the Ref scenario, respectively
Conclusion
In present work, WTP functions were typically built yet incorporated into energy model for estimation of WTP impacts on energy use and evaluation of optimal energy use pathways.

## Slide 19
Thanks for your attention !
国立環境研究所
国立研究開発法人
NATIONAL INSTITUTE FOR ENVIRONMENTAL STUDIES
Lu GAO, Yuki HIRUTA and Shuichi ASHINA
ACKNOWLEDGMENT: This research was supported by Environment Research and Technology Development Fund (2-1711) of Environmental Restoration and Conservation Agency and Ministry of the Environment Japan.