## Slide 1: IAEE 2021 Online Conference
Optimal supply chains and power sector benefits of green hydrogen
Fabian Stöckl. Wolf-Peter Schill, Alexander Zerrahn
June 9, 2021
https://arxiv.org/abs/2005.03464
Notes: Joint work with my great co-authors at DIW Berlin
Outcome of BMBF Kopernikus project

## Slide 2: Research questions and contribution
Sector coupling as a strategy to
(i) decarbonize other sectors
(ii) provide flexibility to the power sector  often under-represented in models
Focus here: hydrogen
Domestic (German) H2 production and distribution, use for fuel-cell electric vehicles
We determine least-cost hydrogen supply chains
Considering differences in energy efficiency, investment costs, and storage capabilities
Considering electricity system interactions  main contribution
1
Notes: Not particularly convinced that fuel cells are the way to go for vehicles…

## Slide 3: Model: extension of DIETER
This calls for a numerical model
Extension of open-source model DIETER, co-optimization of power and hydrogen sector
https://gitlab.com/diw-evu/dieter_public/dietergms/-/tree/1.4.0 https://doi.org/10.5281/zenodo.3693306
New hydrogen module
Four channels for distributing H2 to fuel stations
  Decentral electrolysis
  Central + gaseous H2
  Central + liquified H2
  Central + LOHC
Applied to 2030 scenario for Germany
RES shares between 65% and 85%
Hydrogen demand: 0, 5%, 10%, 25% of passenger road traffic (0, 9, 18, 45 TWhH2)
2
https://commons.wikimedia.org/wiki/File:Dibenzyltoluene_V1.svg
Notes: Who has ever heard about LOHC?

## Slide 4: Overview of hydrogen supply chains in the model
2
 We do not investigate all channels in one model run, but combinations of each centralized with the decentralized channel
Notes: General picture: three centralised vs one decentralised channel
Always dec+cent for numerical reasons
 All come with different cost parameters
[PEM vs. ALK: PEM more expensive, but higher efficiency [chlor-alkali]]
LH2: storage loss
LOHC: hydrogenation exothermal
[Different costs of trailers]
LOHC: electricity needed for dehydrogenation
Only PEM for decentralized electrolysis

## Slide 5: Results: hydrogen supply chains and H2 supply costs
3
Low RES share, low H2 demand:
Not much need for additional flexibility
Decentralised H2 supply dominant because high energy efficiency matters most
Notes: How to read this: for each combination of dec-cent, shares; plus H2 system costs (lower is better; calculated by comparing total system costs with baseline)
What happens:
Low Res, low H2 demand: dec
Increasing RES shares (to the right): LH2
Increasing H2 demand: LH2 (or LOHC)
(- H2 system costs decrease with RES, but increase with dem)
More flexible: electricity use for hydration more temporally de-coupled from H2 demand ( after first storage)
  Decentral supply chain most efficient in terms of overall energy demand in 〖𝑘𝑊ℎ〗_𝑒𝑙∕〖𝑘𝑊ℎ〗_𝐻2
  LOHC has favorable combination of total energy demand and energy demand at filling station
  GH2 and LH2 both energy efficient and low electricity demand at filling station – but high storage costs
- GH2 and LH2 only with expensive storage if no cheap caverns available!

## Slide 6: Results: hydrogen supply chains and H2 supply costs
3
High RES share, low H2 demand:
Higher renewable surplus generation
Temporal flexibility more beneficial
LH2 (and LOHC) allow cheaper longer-term storage
Notes: More flexible: electricity use for hydration more temporally de-coupled from H2 demand ( after first storage)
  Decentral supply chain most efficient in terms of overall energy demand in 〖𝑘𝑊ℎ〗_𝑒𝑙∕〖𝑘𝑊ℎ〗_𝐻2
  LOHC has favorable combination of total energy demand and energy demand at filling station
  GH2 and LH2 both energy efficient and low electricity demand at filling station – but high storage costs
- GH2 and LH2 only with expensive storage if no cheap caverns available!

## Slide 7: Results: hydrogen supply chains and H2 supply costs
3
High H2 demand:
LH2 again most beneficial
GH2: high storage and transportation costs
Notes: LH2 suffers from boil off (no option for seasonal storage)  LOHC gets relatively better
More flexible: electricity use for hydration more temporally de-coupled from H2 demand ( after first storage)
  Decentral supply chain most efficient in terms of overall energy demand in 〖𝑘𝑊ℎ〗_𝑒𝑙∕〖𝑘𝑊ℎ〗_𝐻2
  LOHC has favorable combination of total energy demand and energy demand at filling station
  GH2 and LH2 both energy efficient and low electricity demand at filling station – but high storage costs
- GH2 and LH2 only with expensive storage if no cheap caverns available!

## Slide 8: Effects on generation capacity (vs. baseline without hydrogen)
4
Larger effects with growing hydrogen demand
Smaller effects with growing RES penetration (better utilization)
Hydrogen favors PV deployment
Notes: Now, changed setup: H2 demand increases to the right, RES share to the bottom

## Slide 9: Effects on yearly generation and curtailment (vs. baseline w/o hydrogen)
4
Flexible H2 supply chains integrate RES that would otherwise be curtailed
LOHC has the largest capability for this
„Mixed blessing of flexibility“: also helps integrating lignite
Notes: Benefits in 80% scenario driven by taking up surplus generation

## Slide 10: Two complementary metrics of CO2 emission intensity
4
Chart: kgCO2 per kgH2
| Res65-Dem5 | Res65-Dem10 | Res65-Dem25 | Res70-Dem5 | Res70-Dem10 | Res70-Dem25 | Res75-Dem5 | Res75-Dem10 | Res75-Dem25 | Res80-Dem5 | Res80-Dem10 | Res80-Dem25
OS+GH₂ | 7.8323 | 7.8798 | 9.7772 | 6.3641 | 6.3317 | 7.7597 | 8.5062 | 7.277 | 6.7606 | 12.107 | 12.2988 | 10.7363
OS+LH₂ | 7.8323 | 8.198 | 8.5653 | 6.3641 | 7.7375 | 8.3467 | 11.1592 | 11.6946 | 9.8724 | 12.5479 | 12.8664 | 12.9453
OS+LOHC | 7.8323 | 7.8798 | 10.3715 | 6.3641 | 6.4053 | 8.399 | 10.3307 | 8.1877 | 7.331 | 11.7569 | 12.3333 | 10.9624
Chart: kgCO2 per kgH2
| Res65-Dem5 | Res65-Dem10 | Res65-Dem25 | Res70-Dem5 | Res70-Dem10 | Res70-Dem25 | Res75-Dem5 | Res75-Dem10 | Res75-Dem25 | Res80-Dem5 | Res80-Dem10 | Res80-Dem25
OS+GH₂ | 11.3818 | 11.3 | 11.604 | 9.9282 | 9.8434 | 9.9656 | 9.4291 | 8.9895 | 8.7009 | 7.3783 | 7.5131 | 7.4029
OS+LH₂ | 11.3818 | 11.6093 | 11.9337 | 9.9282 | 10.2855 | 10.4725 | 10.326 | 10.2195 | 9.6104 | 7.9807 | 8.0647 | 8.0429
OS+LOHC | 11.3818 | 11.3 | 11.694 | 9.9282 | 9.9007 | 10.3364 | 11.2449 | 9.9972 | 9.1622 | 8.3659 | 8.506 | 7.9865
Additional System Emission Intensity of Hydrogen (ASEIH)
Average Provision Emission Intensity of Hydrogen (APEIH)
Increase with RES share (lignite effect)
Decrease with RES share
Notes: ASEIH: Total emission effect vs. Baseline w/o H2  takes full power system effects into account
APEIH: Average emissions prevailing in hours of production (and distribution)
Careful when interpreting emissions results! Both views are valid.
CO2 price 30 €/t

## Slide 11: Two complementary hydrogen cost metrics
4
Chart: €/kg
| Res65-Dem5 | Res65-Dem10 | Res65-Dem25 | Res70-Dem5 | Res70-Dem10 | Res70-Dem25 | Res75-Dem5 | Res75-Dem10 | Res75-Dem25 | Res80-Dem5 | Res80-Dem10 | Res80-Dem25
OS+GH₂ | 5.4208 | 5.5354 | 6.5704 | 5.6008 | 5.7079 | 6.61 | 6.179 | 6.1248 | 6.4877 | 5.9221 | 6.3035 | 6.4733
OS+LH₂ | 5.4208 | 5.5237 | 5.6182 | 5.6008 | 5.672 | 5.7566 | 5.8634 | 5.9663 | 5.9432 | 4.5938 | 5.5632 | 6.0984
OS+LOHC | 5.4208 | 5.5354 | 7.0256 | 5.6008 | 5.7155 | 6.8858 | 6.1034 | 6.0421 | 6.7142 | 4.7797 | 5.1646 | 6.2494
Chart: €/kg
| Res65-Dem5 | Res65-Dem10 | Res65-Dem25 | Res70-Dem5 | Res70-Dem10 | Res70-Dem25 | Res75-Dem5 | Res75-Dem10 | Res75-Dem25 | Res80-Dem5 | Res80-Dem10 | Res80-Dem25
OS+GH₂ | 0.13144 | 0.1991 | 0.67893 | 0.19552 | 0.26092 | 0.7401 | 0.70659 | 0.56595 | 0.7703 | 1.2509 | 1.3496 | 0.99498
OS+LH₂ | 0.13144 | 0.19015 | 0.20797 | 0.19552 | 0.24111 | 0.26398 | 1.2303 | 0.90847 | 0.55918 | 1.7051 | 1.9777 | 1.3703
OS+LOHC | 0.13144 | 0.1991 | 1.051 | 0.19552 | 0.26899 | 1.0125 | 1.595 | 1.0113 | 1.1571 | 1.3149 | 1.4499 | 1.4484
Average Provision Costs of Hydrogen (APCH)
Difference between APCH and Additional System Costs of Hydrogen
Slight increase with demand
ASCH much smaller for high RES shares
Notes: APCH: producer / consumer perspective: (ann. H2 infrastr. + yearly electr. costs for H2) / total H2 supply
ASCH: power sector perspective: delta system costs / hydrogen supply  total power sector benefits
Costs are below the uniform retail price of hydrogen in Germany of around 9.5€/kg by 2020

## Slide 12: Effects of hydrogen on system costs of electricity (vs. baseline w/o hydrogen)
4
Chart: 
| Res65-Dem5 | Res65-Dem10 | Res65-Dem25 | Res70-Dem5 | Res70-Dem10 | Res70-Dem25 | Res75-Dem5 | Res75-Dem10 | Res75-Dem25 | Res80-Dem5 | Res80-Dem10 | Res80-Dem25
OS+GH₂ | -0.00040434 | -0.00017548 | 0.00056077 | -0.00033386 | -0.00013466 | 0.0016367 | -0.015567 | -0.018455 | -0.028903 | -0.025857 | -0.049012 | -0.072716
OS+LH₂ | -0.00040434 | -0.0015151 | -0.0065912 | -0.00033386 | -0.0037223 | -0.011781 | -0.023457 | -0.032125 | -0.040736 | -0.037693 | -0.067183 | -0.085688
OS+LOHC | -0.00040434 | -0.00017548 | 0.012297 | -0.00033386 | -0.001158 | -0.0043115 | -0.031831 | -0.036387 | -0.040841 | -0.031993 | -0.062026 | -0.09314
Benefits increase with RES shares because of better use of surpluses
Notes: Total power sector costs, excluding investment, fixed and (non-electricity) variable costs of hydrogen supply chain  benefits completely attributed to power sector
Calculation: (total system costs – fixed h2 infrastructure costs) / total generation
( we assume h2 infrastructure is not made for power system)

## Slide 13: Summary and conclusion
Trade-off between energy efficiency and temporal flexibility
Energy-efficient decentral electrolysis optimal for lower RES shares
Less energy-efficient but more flexible centralized electrolysis better for higher RES shares
Possible co-benefits of green H2 for RES integration
Depend on storage capability of supply chain
„Mixed blessing“: additional flexibility may also benefit dirty generators
Different cost metrics raise complementary insights
Limitations
Results driven by renewable surplus, no competing sector coupling options
Limits to RES capacity deployment in Germany (and Europe)
5

## Slide 14: Want to read the full paper?
Open-access preprint: https://arxiv.org/abs/2005.03464
Forthcoming gold open access version in Scientific Reports
5

## Slide 15
Dr. Wolf-Peter Schill wschill@diw.de | @WPSchill

## Slide 16
Notes: PEM vs. ALK: PEM more expensive, but higher efficiency [chlor-alkali]
LH2: storage loss
LOHC: hydrogenation exogenous
Different costs of trailers

## Slide 17
Notes: LOHC: electricity needed for dehydrogenation
Only PEM for decentralized electrolysis

## Slide 18: Data and scenarios
Electricity sector
Brownfield scenario for 2030
Capacities bounded by current grid development plan (NEP)
Maximum investment into thermal plants, minimum investments into renewables and storage
Time series provided by Open Power System Data & ENTSO-E
Exogenous minimum renewables share of 65%, 70%, 75%, 80%
2
Hydrogen infrastructure
Fully „greenfield“
H2 demand for mobility: 0, 5%, 10%, 25% of passenger road traffic in Germany (0, 9, 18, 45 TWhH2)
General assumptions: each fuel station can only offer H2 from one channel
Chart: 
| Lignite | Hard coal | CCGT | OCGT | Oil | Other | Biomass | Run-of-river | Wind onshore | Wind offshore | PV | Pumped hydro storage | Li-ion batteries
 | 9.3 | 9.8 | 17.6 | 17.6 | 3.2 | 4.1 | 6 | 5.6 | 81.5 | 17 | 91.3 | 9.5 | 2
Notes: NEP 2019, scenario B
Lower bounds for vRES and storage
Upper bounds for conventional, bio and pumped hydro

## Slide 19: Background
Some intuition: potential drivers of results
1

## Slide 20: Drivers I: Tradeoff between overall efficiency and flexibility
3
Chart: overall elecricity demand of hydrogen supply chains (kWhel/kg)
| 50.474037660131614
dec | 50.474
gh2 | 3.9108
lh2 | 1.0332
lohc | 14.1764
lh2-max | 1.0332
lohc-max | 14.1764
more flexible
more energy efficienct
Notes: DEC: most efficient, but highest electricity demand at the time of re-fueling
Other options: more flexible, but less energy efficient
LOHC dominated  you would not expect to be part of the solution
More flexible: electricity use for hydration more temporally de-coupled from H2 demand ( after first storage)
  Decentral supply chain most efficient in terms of overall energy demand in 〖𝑘𝑊ℎ〗_𝑒𝑙∕〖𝑘𝑊ℎ〗_𝐻2
  LOHC has favorable combination of total energy demand and energy demand at filling station
  GH2 and LH2 both energy efficient and low electricity demand at filling station – but high storage costs
- GH2 and LH2 only with expensive storage if no cheap caverns available!

## Slide 21: Drivers II: Fixed investment and transportation capacity costs
Only 3% spread between cheapest and most expensive supply chain
Transportation costs highest for GH2 , low effective load capacity of GH2 trailer
3
Chart: unweighted fixed costs (€/kW) with(out) transportation
| DEC | GH₂ | LH₂ | LOHC
 | 27327.3003 | 27774.5223 | 28151.4512 | 27897.51
 | 27327.3003 | 27591.2739 | 28114.4549 | 27854.6143
Chart: transportation capacity costs (€/kgH2)
| GH₂ | LH₂ | LOHC
 | 1228.7771 | 261.7738 | 248.6418

## Slide 22: Drivers III: Storage costs (and losses)
Substantially lower storage costs for LH2 and LOHC
Expensive high pressure storage at the filling station  only buffer storage
LH2 also suffers from boil-off
 Intuition not so clear  Analysis with numerical optimization model required
3
Chart: storage costs (€/kg)
| DEC (only HP) | GH₂ | LH₂ | LOHC | High Pressure
 | 18.362 | 13.771 | 0.407 | 0.306 | 18.362
filling station