## Slide 1
Planning Electric Vehicle Charging Infrastructure in a Transitioning Community
Eric Hittinger1,2, Alain Bouscayrol1, Elodie Castex3
1 Univ. Lille, Arts et Metiers Institue of Technology, Centrale Lille, Yncrea Hauts-de-France, ULR 2697 – L2EP, F-59000 Lille, France
2 Department of Public Policy, Rochester Institute of Technology, Rochester, NY, USA
3 Univ. Lille, ULR 4477 – TVES – Territoires Villes Environnement & Société, F- 59000, Lille, France

## Slide 2: Some background on CUMIN and TESS
CUMIN: Campus of University with Mobility based on Innovation and Neutral in carbon
Objective: reduction of the GHG emission due to transport to/within the campus
Motivation: The 22,000 person “Cité Scientifique” campus has a carbon footprint that is ~50% from private commuter vehicles
TESS: Technical Economic Study of Sustainable campuses
Objective: create techno-economic tools to study the costs to commuters and university administration of different vehicle electrification plans
One important part is understanding what infrastructure the university should build and when they should build it

## Slide 3: Campus “Cité Scientifique” Université de Lille – a large suburban campus
22 000 users
80 buildings
110 ha

## Slide 4: Transportation is the largest source of greenhouse gases for the campus (ULille, campus Cité scientifique)
[Bilan Carbone, Lille1, COMUE 2015]
4
56%
97 % home-university trips
Passenger cars: 27% of travel
78% of pollution
soft
mobility ?
electric
vehicles ?
public
transportation?
local
accommodation?

## Slide 5: The literature around charging infrastructure generally assumes a fixed demand for charging, but this isn’t realistic
There is a large body of literature on EV charging infrastructure, mostly studying one of these:
Optimal operation of a given set of infrastructure
Grid integration possibilities of charging infrastructure
Optimal design of infrastructure needed for a given EV charging demand

## Slide 6: Research Question: What infrastructure (charging stations, solar PV, and storage) should the university build in response to a growing EV demand?
What infrastructure should be built and when should we build it, given things like economy of scale and falling costs of new technology?
Is it better to buy clean electricity from grid suppliers or generate it locally?
What business model for charging will attract commuters while raising some income?

## Slide 7: The central part of the model uses an hourly “dispatch model” to route power between energy sources and EVs
Vehicle Parameter | Range of Values
Home-work distance | 0-50 km
Battery Size | 10-90 kWh
Arrival time at work | 6h – 10h
Departure time from work | 16h – 20h
Efficiency | 200 Wh/km
Charge rate | 3.5 kW if battery < 20 kWh 7 kW if battery ≥ 20 kWh

## Slide 8
An example week of operation shows the general concept: Premium customers are reliably charged while Free-charging customers receive excess solar energy

## Slide 9: Solar PV, battery storage, and EV chargers are modeled with both economy of scale and falling prices over time
kW of PV | $/W (in 2018)
5 | $2.80
50 | $2.00
500 | $1.45
5,000 | $1.05
Solar PV economy of scale
Solar PV price decline
3.75% per year (after 2018)
kWh of storage | $/kWh (in 2018)
10 | $1,700
100 | $1,214
1,000 | $900
Battery economy of scale
Battery price decline
6.3% per year (after 2018)

## Slide 10: The dispatch model is used within an optimization that searches for the lowest-NPC “buildout plan” for chargers, solar PV, and stationary storage

## Slide 11: In a scenario with continual growth in EVs, the optimal strategy is to build chargers and solar PV every ~10 yrs

## Slide 12: One feature of the model is how it responds to uncertainty in future demand
Each line is a “buildout plan” for chargers, but the red line shows what was actually built. The model “plans” 20 years out, but only “commits” to next year’s chargers. It can adjust the plan each period.

## Slide 13: As changes in demand are observed, the optimization shifts timing and amount of solar PV

## Slide 14: Thank You!