## Slide 1: NUDGING OCCUPANTS’ BEHAVIOUR TOWARDS LESS ENERGY CONSUMPTION IN BUILDINGS
Rabab Akkouche, Sandrine Selosse, Gilles Guerassimoff MINES ParisTech, PSL Research University, Centre for Applied Mathematics, Sophia Antipolis
09/06/2021

## Slide 2: General Context

## Slide 3
Chart: FINAL ENERGY CONSUMPTION BY SECTORS TOTAL : 144 Mtep in 2018
| Tertiary - Residential | Industry | Transport | Agriculture
CONSOMMATION FINALE ÉNERGÉTIQUE PAR SECTEUR TOTAL : 144 Mtep en 2018 | 46 | 19 | 32 | 3
Source : calculs SDES, d’après les sources par énergie
1
      General Context

## Slide 4
Improve energy efficiency in buildings
Performance of the envelope
Insulation
Architecture
« Bioclimatic » Design
Performance of materials
The building
Active Energy Efficiency
Technological solutions
Monitoring
Energy consumption regulation and control
Efficient equipments
      General Context
1

## Slide 5
1
Understand
Model
Predict
Change
Evaluate
Occupant behavior
Indoor Comfort
Crucial factors influencing real energy consumption in buildings
      General Context
Survey
Data Collection
Dynamic Thermal Simulation
Behavioural models
NUDGES
Data Collection
Dynamic thermal simulation

## Slide 6
Nudges
Experimentation
Dynamic Thermal Simulation
Dynamic Thermal Simulation (DTS) is used to predict the way a building responds when subject to external environmental factors
It is also a way to prove the energy performance of buildings and achieve certain ratings.
      General Context
1

## Slide 7: Dynamic Thermal Simulation: Case study: Office building

## Slide 8
Office building
3 floors
1 meeting room
1 kitchen
34 Offices
Localisation: Nice, France
50 Occupants
2
      Dynamic thermal Simulation

## Slide 9
Increasing energy performance of the building:
Performance of materiels
Efficient Equipements ( Heating + Cooling )
Perfomance of Windows
Insulation
19% of energy consumption reduction
2
      Dynamic thermal Simulation

## Slide 10
Behaviour Change | Heating | Cooling | Lighting | Devices
Base case | 21 C° Winter | 23 C° Summer | Lighting ON all day: 8h – 18h | Phone Computer + 2 Screens ON: 8h – 18h STAND BY after work hours
Intervention 1 | Night / Weekend Mode: 16 C° Absence more than 2 days: 8 C° | No cooling at night Open windows at night | - Switching off lighting when leaving office | - Switching off computers when leaving office
Intervention 2 | - Turn off heating if a window is open | Open windows in the morning with no cooling Using shutters |  | 
Intervention 3 | Close shutters in winter evenings Turn Off Heating 1 hour before the office |  |  | 

## Slide 11
Chart: Energy savings based on behavior change for the different systems
| Heating | Cooling | Lighting | Equipements | All systems
Base case | 18932 | 20353 | 8875 | 24526 | 72685
Interventions 1 | 10136 | 19165 | 4889 | 3356 | 53514
Interventions 1 and 2 | 9995 | 18928 | 53136
Interventions 1, 2 and 3 | 9432 | 52573
2
      Dynamic thermal Simulation

## Slide 12
Chart: Energy savings based on behavior change in different offices
| All offices | South Offices | North Offices
Base Case | 72685 | 72685 | 72685
Interventions 1 | 53514 | 68613 | 69574
Interventions 1 and 2 | 53136 | 66933 | 67334
Interventions 1 , 2 and 3 | 52573 | 65343 | 66445
2
      Dynamic thermal Simulation

## Slide 13
Energy saving interventions applied to all the offices
Heating : 50% of reduction
Cooling : 7% of reduction
Lighting : 45% of reduction
Total : 28 % of reduction
In South Offices:
Total Reduction of : 10%
In North Offices :
Total Reduction of: 8%
2
      Dynamic thermal Simulation

## Slide 14: Experimentation

## Slide 15
Collect information about occupants
Understand occupant’s interaction with the building and energy use
Identify energy consuming behaviours
Understand the gap between intentions and actions
Understand energy reduction importance for occupants
Comfort perception and actions
Understand occupants motivations to change behaviours
Draw occupants profiles
      Survey
3
Tell me about YOU
Building and YOU
Comfort and YOU
Energy and YOU
Intentions VS Actions

## Slide 16
Data Collection
Door opening
Window opening
Temperature set point
Occupancy
Energy consumption
      Data collection
3

## Slide 17
NUDGE
A low cost solution
Use of cognitive biases
No use of financial incentives or order
Doesn’t affect choices based on explicit preferences
“To count as a mere nudge, the intervention must be easy and cheap to avoid. Nudges are not mandates. Putting fruit at eye level counts as a nudge. Banning junk food does not.” [Thaler et Sustein , 2008]
Transform incentives to actions by making individuals choose the wished decision
4
      NUDGES

## Slide 18
Peer to peer comparison
Giving suggestions in order to reduce consumption
Feedback
Giving feedback to occupants about their energy use
Moral appeal
Messages expressing a responsible consideration and human consequences of global warming
Using pictures
Comparing occupants’ consumption to their colleagues
Benchmarking eco-friendly behaviours of other occupants
Tailored messaging
Social reviews
Defining right behaviors adopted by the majority
Applying different types of Nudges to different offices
Adapting Nudges to energy consumption evolution
4
      NUDGES

## Slide 19: Conclusions and perspectives

## Slide 20
      Conclusion and Perspectives
5
Importance of changing occupants’ behaviors in reducing energy consumptions in tertiary buildings
Impact of offices location in reducing energy consumption
Importance of identifying occupants profiles for more energy reductions
Integrating behavior models in order to have more accurate results in predicting energy consumptions
Defining occupants’ patterns depending on experimental results in order to quantify the impact of Nudges
Suggesting the type of Nudges to use depending on occupant’s response to the different intensives used